# Notes Bachelor Thesis Presentation

### Slide 2
Condition of a Lithium Ion Battery
durability: how the internal behaves over time regarding aging

### Slide 3
Build of a lithium Ion Battery
Aging Process → What makes a Lithium Ion Battery age?
Meaning of the internal restistance

### Slide 4
Aging Process → Temperature, Cycle of Charging and Discharging, just an example from literature

### Slide 5
HPPC → long preperation time, example from the literature, parameters can be different for the measurement, repeating the right part until the battery reaches 10% of State of Charge, then repeat the measurement for increasing the State of Charge until 90%

### Slide 6
Galvanostatic Intermittent Titration Technique (GITT) → Similar to the HPPC method, but a the behaviour of the material of the electrodes are important, therefore a model has to be created, chemical diffusion coefficient, thermodynamic properties of the electrode material → better understanding of electrochemical behaviour
Electrochemical Impedance Spectroscopy → loaded with a sinusoidal excitation signal, voltage response is measured, often overlayed with different DC layers to tests diverse loads, shows the beheaviour at different frequencies

### Slide 7
Calorimetric Measurment → temperature exchange between the surface temperature of the cell and the wall of the calorimetric chamber

### Slide 8
Findings → SEI Layer (solid electrolyte interphase) is the passivation layer
charge passage → flow of electric charge through phase boundary
Diffusion in Equilibrium → through the separator
### Slide 9
### Slide 10
### Slide 11